## Slide 1: Wii Interactive White Board Presentation
http://wiiteachers.com

## Slide 2: A Wii remote – $40
Don’t Be Generic!!
Make sure you use
NEW batteries.
Upgrade to power pack.
Notes: Don’t use a generic remote because I did and I couldn’t get it to work. You don’t want the reason it is not working is that your batteries are dead. Also, I think it needs to be synced to an actual wii before you use it….not sure though. If you are just starting out, just use batteries and not the rechargeable powerpack. Keep it simple at first. You can always upgrade to those things once you have it running.

## Slide 3: A Bluetooth connection – $10
Try it first.
Control panel. Look for the bluetooth logo.
The mini usb Bluetooth dongle
from wiiteachers works great.
Notes: Most lap tops have these already built in. But if you don’t have them, you can buy one on the wii teacher web site. I have noticed that MACs recognize the wiimote very quickly while PC’s have trouble. Check your laptop control panel. Have it set to the classic view. Follow the directions on the next slide. If it doesn’t work, you will want to get the mini usb Bluetooth dongle off the website and it works great. I think this is one of the biggest problems that I have seen for $10 its not a bad idea to get this.

## Slide 4: Connect your wiimote to your computer
Put your wiimote in discovery mode by pressing the 1 and 2 buttons simultaneously. The blue lights will flash. They need to stay on until your mote is discovered so you may want to keep holding these down until you are connected.
Control Panel
BlueTooth Devices
Add a wireless Device
Nintendo RVL – CNT – 01
Don’t use a Passkey
Properties
Services
Make sure keyboard is selected
This is a ONCE and DONE procedure and probably the most ‘glitchy’ part of the process!!

## Slide 5: “The Spot” wiimote mount and mini tripod - $23
Notes: This is a holder for your Wii remote. I am sure that you can make one if you are pretty handy. But the one they have on the website is pretty cheap and it works GREAT. So I would recommend this purchase.

## Slide 6: An IR pen - $10 - $30
Make your own!! Science Project ??
Or Be LAZY……. Like ME!!
Notes: There are websites to make these (just google “make your own IR pen”). If you work at a high school and want to have the science teacher have them make them for you, great. If not just get them from the website. They are pretty cool. The cheap ones use the cell batteries which are sometimes harder to find. The middle and upper range ones use AAA batteries and are easier to replace. Some people think that it is hard to press the button that sticks up and so for those people I would recommend spending the extra money to buy “the groove” since it is flat.

## Slide 7
Get out your cell phone cameras!!
Notes: TROUBLE SHOOTING: To be sure that your pen is working, hold it up to your cell phone camera. Cameras can detect infrared light and you will be able to see whether your pen is working or not…. Be sure that you are actually pressing the button on the pen!!

## Slide 8: Download Smoothboard 1.6 $30
Notes: Try it out first. If you are going to use it then buy the it. If you use the unregistered version, it will ask you everytime you open it if you want to register yet. Then once you open it, the smoothboard logo will float around on the right side of your screen. It moves around so your work will never be permanently covered but it can be a little annoying.

## Slide 9: HARDWARE
A laptop and a projector. You do NOT need a screen or whiteboard - just use the WALL!!
?
Notes: The thing that sets this wii technology apart is that you don’t need a whiteboard or a screen. All you need is a wall. This makes it a great technology for learning centers and presentations.
You can use a screen, white board, or wall with this. You can even turn your computer monitor into a touch screen or maybe even point the projector down on a table and you can use a table top surface. The screen is probably the least effective because it sways and can cause problems with calibration. Using a whiteboard is nice because if you are not comfortable using the IR pen to write with and you don’t need to save your mark-ups, you can just write with the white board dry erase markers.

## Slide 10: What You Need:
Wii Remote – Steal your kid’s or $40
Bluetooth – Free or $10
Wiimote Mount – not essential or $23
IR pen - $10 – $30
Smoothboard software – Free to start or $30
MATH:
Notes: Minimum cost is $10. Maximum cost is $133. Not bad. So say $150 with shipping and handling…. Price the SMART, Promethean or Mimio’s….. Not bad!!

## Slide 11: Open Smoothboard
Make sure your wiimote lights are still flashing so that it can be discovered.

## Slide 12: CALLIBRATE YOUR SCREEN
Press the A button on your wiimote or use the smoothboard operation.
If you can not callibrate, you need to adjust your wiimote angle and then RECALLIBRATE!!
You can’t move your wiimote half way through a callibration!!

## Slide 13: Adjusting Screen Size
In Smoothboard
  Show settings
  Screen
  Track partial screen area
  Select screen area to track
  Click and drag on desired area
  RECALLIBRATE!!
Notes: You will need to adjust your screen size if you are using a projector and screen where the top of the screen is out of your reach. Because the callibration requires you to touch the 4 extreme corners of the screen, you will not be able to callibrate unless you adjust your screen size. You will also have to adjust your presentations because you will not be able to interact with the top of the screen. If you are the only one using your room, you could see if you could have the projector adjusted to not take up the whole screen.

## Slide 14: Using the IR Pen on the Wii IWB (IR= infra-red, IWB = interactive white board)
Tilt the pen so that it can be read – writing straight on does not work well.
How you stand and interact with the Wiimote IWB while presenting will have a significant impact on how often you block with the Wiimotes field of view. Sometimes just rotating your non writing shoulder slightly away from the whiteboard ensures perfect tracking.

## Slide 15: Import into Power Point:
You can use smoothboard to write in additional notes to your power point.
Felt tip pen
White screen
Make any mark-ups that you want on your white screen. When you are done. Use the arrow buttons underneath the word “power point” on your smoothboard tool bar to arrow over to “annotation”. In the annotation screen, click on snapshot. Your mark-ups will be saved in your mark-ups folder.
When you are done at the end of the day and want to import these mark-ups into your power point, you can find your snapshots in:
  Smoothboard
  File
  Open snapshots folder
  Right click on the snapshot you want
  Copy
  Paste into your power point

## Slide 16: Math Applications:
TI-Smartview
TI-Nspire Computer version
Geogebra – FREE
SMARTboard graphics - EXPENSIVE …free trial available. Student version is $35.
ActivInspire is Free